PLANETARY DATA SYSTEM

          USER'S GUIDE FOR THE PDS IMDISP PROGRAM

                         INTRODUCTION

     This  document describes the IMDISP program, an  interactive 
image  display utility for the IBM Personal Computer family  (PC, 
XT  and AT) and compatibles. It has been developed for  use  with 
the  Compact  Disk  - Read-Only Memory  (CDROM)  storage  systems 
currently being evaluated by the Planetary Data System (PDS).  It 
can  also  be  used to display images stored on  floppy  or  hard 
disks.

     This  User's Guide presents an overview of image  processing 
and  CDROM fundamentals, a section on the installation of  IMDISP 
and CDROM software and hardware, a description of IMDISP  program 
operation,  a description of other utility programs which can  be 
used in conjunction with IMDISP, and a command summary.

     Appendices  are provided which describe the contents of  the 
IMDISP distribution disk, the contents and format of the  Voyager 
Uranus   and   Interactive  Data  Interchange  CDROM   disks,   a 
description  of  the  data labeling  standards  and  image  file 
formats  found on these CDROM disks, and references  for  further 
information about image processing and CDROMs.

     Other  support  software for using the PDS CDROM  disks  has 
also  been developed. These packages include the  USGS  Planetary 
Image Cartography System (PICS) for Microvax computers, a set  of 
FORTRAN routines to access CDROM disks on VAX computers  (VMSCD), 
and "C" language source code to process disks written in the High 
Sierra  format. Contact Mike Martin (JPLPDS::MMARTIN) for  access 
to these tools.


                           Chapter 2

                          BACKGROUND


     Efforts  to utilize small computer systems for  display  and 
analysis  of  scientific data have been hampered by the  lack  of 
sufficient  data  storage  capacity to  accommodate  large  image 
arrays.  Most  planetary images  require  nearly  a  megabyte  of 
storage. Over the past two years a new storage technology "CDROM" 
has been developed which provides the capability to store  up  to 
600  megabytes of data on a single 4.72-inch disk. The disks  can 
be  mass  produced,  and  hundreds of  copies  of  large  digital 
archives distributed rather than the few sets currently produced. 
Readers for CDROM disks can now be purchased for under a thousand 
dollars   for  use  on  personal  computers  and   some   science 
workstations.

     The  PDS  has  worked with  industry  and  other  government 
agencies  to  support the development of CDROM as  a  major  data 
distribution  and storage media for space science  data.  Initial  
development  efforts by the PDS, the Voyager Project, and  multi-
disciplinary   science  representatives  have  resulted  in   the 
production  of 2 CDROM disks, one containing 800  digital  images 
from   the  Voyager  Uranus  encounter,  and  one  containing   a 
collection  of more than 1,400 data files from   all   scientific 
disciplines.  The IMDISP program can be used to display  most  of 
these  data  files on a personal computer equipped with  a  CDROM 
drive.

2.1 DIGITAL IMAGE PROCESSING SUMMARY

     A digital image is a picture converted to numerical form  so 
that  it  can  be stored and used in a  computer.  The  image  is 
divided  into a matrix of small regions called picture  elements, 
or pixels. The rows and columns of pixels are called "lines"  and 
"samples", respectively. Each pixel has a numerical value, or  DN 
(data number) value, quantifying the darkness or brightness of    
the image at that spot. In total, each pixel has an address (line 
number,  sample  number) and a DN value, which is all  that  the 
computer needs for processing. The DN value of each pixel usually 
represents  a shade of darkness or brightness between  black  and 
white  (gray levels). How many gray levels there are in an  image 
depends  on  the  number of bits used  to  represent  each  pixel 
intensity  in  the computer. The number of gray  levels  will  be 
equal to 2^n, where n is the number of bits per pixel's DN value. 
If 8 bits are used to represent a pixel's DN value (gray  level), 
the  system will be capable of using 2^8, or 256, gray levels  in 
an image, where DN 0 is pure black, and DN 255 is pure white. If 
each DN used only 4 bits of storage, the image would contain only 
2^4 or 16 gray levels; if there were only 1 bit per DN, the image 
would contain only black and white pixels (bit values of 0 or 1).

2.2 OVERVIEW OF IMDISP CAPABILITIES

     While  the  specifics of IMDISP commands  are  discussed  in 
Chapter 4, this section provides a general overview of how a user 
can manipulate images once a file is selected. There are  DISPLAY 
commands which allow the user to display all or part of an  image 
at  various  positions on the display screen. The user  may  also 
zoom in and out from a point on the image defined by the  cursor, 
and may pan around the image. The cursor may be turned on or off; 
when  on, the arrow keys are used to move the cursor  around  the 
screen; when off, the cursor is not visible.

     A  user may choose to "subsample" the image, to enable  more 
or  all  of the original image to be displayed on the  screen  at 
once. For example, if the image were subsampled by a factor of 2, 
every  other  pixel  from every other line  would  be  displayed, 
starting from the upper left corner of the image. If a factor  of 
3  were chosen, every third pixel from every third line would  be 
displayed. Any positive integer may be used for subsampling.

     The user may produce a histogram of an image file, which  is 
a  graph showing the number of pixels per DN value, or per  range 
of  DN values, for the entire image. Histograms are  overlaid  on 
top  of the image, but may be removed using the REFRESH  command. 
Subsampling may be specified when computing a histogram to reduce 
the time required for the calculations.

     A  profile may be created which plots DN value versus  pixel 
along a line between two points on the image. After the cursor is 
used to select the two endpoints, the connecting line is drawn on 
the image and the profile is plotted at the bottom of the screen.

     The user may also "stretch" the image, which is analogous to 
turning the contrast knob on a TV set. The user specifies low and 
high  DN values; all pixels with values lower than the  specified 
"low"  become  black, and all pixels higher  than  the  specified 
"high"  value become white. All pixels between the low  and  high 
values are evenly shaded between black and white.

     There  are bookkeeping types of commands, also. These  allow 
the  user to do such things as retrieve a desired image from  the 
CD-ROM,  to  save an image to a file on hard disk, and  to  erase 
only the graphics from the screen or to erase the entire  screen. 
Users  may  execute batch command files to do a series  of  tasks 
automatically.  Lastly, the user may, of course, EXIT the  IMDISP 
program when done.

2.3 GRAY LEVEL AND FALSE COLOR IMAGES

     Most  planetary  images  are composed  of  8-bit  DN  values 
representing monochrome brightness levels in the scene. To obtain 
color  images,  separate images are taken through  color  filters 
(red,  green,  blue) and are then combined by  ground  processing 
systems to produce a true color image. Only a very small fraction 
of planetary images are available in color versions. Most display 
and analysis is done on monochrome images.

     A display with 256 (2^8) gray levels is required to  present 
the information contained in a standard image. However, the human 
eye  can  only distinguish about 32 gray levels.  Thus  5-bit  DN 
values  would satisfy most display  requirements.  Unfortunately, 
computers  are  oriented to the storage of  and  manipulation  of 
items  which are a power of two, and 5-bit pixels would  be  very 
clumsy. The display devices which the IMDISP program supports are 
limited  to 16 gray levels (PGA), 4 gray levels (EGA) or  2  gray 
levels  (CGA).  The  16 gray levels of the PGA  are  adequate  to 
support   image  analysis;  however  4  or  2  gray  levels   are 
practically useless for viewing planetary images. Fortunately the 
EGA display will support 16 different colors, and a color palette 
can  be  selected  which  uses a graduated  scale  of  colors  to 
represent  gray  levels, producing a "false color"  image  (false 
because  the displayed color does not represent the actual  color 
of the scene).

     A  false color image (also called a pseudo color  image)  is 
created from a black and white image by assigning a color (rather 
than a gray level) to each DN value in the image. For instance, a 
DN  value  of 128 could be reassigned to yellow if  the  user  so 
desired.  Ranges of DNs (e.g., 100-125) may also be assigned  one 
color. Pseudo colors get assigned to DN values in a pseudo  color 
table,  which the display program then uses to determine  how  to 
color  the  image  on the monitor. Display  programs  often  have 
preset   pseudo   color  tables  with  commonly   used   DN-color 
combinations, and the user can simply call for one of these  when 
generating  a pseudo color image. The option exists,  of  course, 
for  users  to  generate their own pseudo  color  tables.  Pseudo 
colors are often used to highlight features of an unusual  nature 
in an image.

     Since  the Enhanced Graphic Adapter for the IBM PC  provides 
only 4 gray shades (black, dark gray, light gray and white)  most 
image viewing is done using a pseudo color table which interprets 
gray  levels  as color values ranging from  black  through  reds, 
greens and blues up to white.

2.4 RADIOMETRIC AND GEOMETRIC CORRECTIONS

     All  camera systems have some kind of distortions  in  the 
lens,  in  the  way the shutter works, etc.  Distortions  in  the 
amount  of  fight transferred through the camera to  the  imaging 
plate  are called radiometric distortions.  Geometric  distortion 
affects  the "squareness" of an image, and is detected by  taking 
an image of a geometric grid.

     For  spacecraft  cameras, both types of  distortion  can  be 
measured  before  launch, and in a limited  fashion,  in  flight. 
These measured distortions are saved in digital files. When a raw 
image is received, these "calibration files," as they are called, 
are  subtracted  from  (or  otherwise  applied  to)  the   image, 
effectively  removing radiometric and geometric distortion.  This 
process is called radiometric and geometric correction. Corrected 
images  contain the closest possible representation of the  scene 
being imaged.

2.5 IMAGE FILE FORMATS

     Digital  image files are seldom stored as a simple array  of 
pixels.  Generally there is an area at the beginning of an  image 
file containing descriptive information about the image. This  is 
referred to as a label or header area. Figure 2-1 shows a diagram 
of a simple image format with a label area followed by the  image 
lines.  In practice, images from planetary missions have  a  more 
complicated   format,  due  to  the  need  to  store   additional 
information  to  allow proper interpretation of the  image  data. 
Figure  2-2  shows  the  format of a  Voyager  image,  which  has 
engineering parameters embedded at the end of each image line  to 
form a line suffix area, an engineering trailer record after  the 
last image line, and this is followed by an image histogram.


                 --------------------------      
                |  Labels or Header Area   |    
                |--------------------------|     
                |  Image Array Line 1      |    
                |--------------------------|    
                |  Image Array Line 2      |
                |--------------------------|
                             .
                             .
                             .
                 --------------------------
                |  Image Array Line n      |
                 --------------------------

            Figure 2-1: Simple Image Format

     Different image label formats have been developed for use by 
nearly  all image processing facilities. Two formats  are  widely 
used  within the planetary and astronomy communities: the  VICAR2 
(Video  Image  Communication and Retrieval) labels  used  by  the 
Multi-Mission   Image  Processing  Laboratory  (MIPL)  and   FITS 
(Flexible  Image  Transport)  labels  used  for  astronomy  image 
interchange.  The PDS has developed a label scheme which is  very 
similar  to  these  standards,  called  the  Object   Description 
Language  (ODL). This format attempts to add a broader  range  of 
data  descriptive capabilities to the proven capabilities of  the 
existing label systems. A description of the ODL architecture  is 
given in Appendix D.

     Most of the images stored on the PDS CDROM disks have either 
ODL  or VICAR2 labels. IMDISP will automatically interpret  these 
labels to determine the display format of the image data.

                 --------------------------------------      
                |  PDS ODL Labels                      |    
                |--------------------------------------|     
                |  Image Array Line 1    | Line Suffix |    
                |--------------------------------------|    
                |  Image Array Line 2    | Line Suffix |    
                |--------------------------------------|    
                                  .
                                  . 
                                  .
                 ---------------------------------------
                |  Image Array Line 800  | Line Suffix |    
                |--------------------------------------|    
                |  Image Engineering Trailer           |
                |--------------------------------------|
                |  Image Histogram                     |
                 --------------------------------------

            Figure 2-2: Voyager CDROM Image Format

2.6 CDROM FUNDAMENTALS

     The CDROM disk uses the same basic data storage format as  a 
CD  audio  disk. In fact, data blocks are identified  by  minute, 
second and sector number, following the audio format. Data blocks 
are recorded along a spiral from the inner to the outer radius of 
the  disk. Each raw data block (sector) contains 2,352  bytes  of 
information,  with  304  bytes used for  housekeeping  and  error 
correction  and 2,048 (2K) containing user data. Each data  block 
is  called a sector, and 75 sectors are stored per second.  Since 
the  nominal  playing time of a CD disk is 60 minutes,  the  data 
storage capacity is 75 sectors per second * 60 seconds per minute 
*  60  minutes  or  270,000 sectors.  Thus  the  nominal  storage 
capacity  of a single CDROM disk is 540,000 kilobytes, which  can 
be  extended  to  more  than  600,000  kilobytes  and  beyond  by 
recording more than 60 minutes of data on a disk.

     In  order  to maximize the storage capacity of  CD  disks  a 
constant  linear  velocity (CLV) recording format is  used.  This 
means that the player changes speed (slows down) as it reads from 
the  inside  to the outside of the disk, to maintain  a  constant 
flow  of data under the read mechanism at a speed of  1.2  meters 
per  second.  This is in contrast to most  magnetic  disk  drives 
which  use  constant angular velocity (CAV)  storage,  where  the 
information density is greater on the inner tracks that the outer 
tracks.  While  the use of CLV recording  increases  the  storage 
capacity  of CDROM disks, it reduces access time, since the  disk 
must change speeds as it moves to different positions on the disk 
radius.  The strategy for locating a recorded data block is  also 
more  complicated than with constant angular  velocity  recording 
technology.

     As  a  result  the average access time of  CDROM  drives  is 
between 400 ms and 1 s, and the maximum data transfer rate to the 
host  computer  is  150 kilobytes per  second.  These  rates  are 
approximately  an order of magnitude slower than magnetic  disks. 
Therefore,  the  access mechanisms to disk directories  and  data 
must  be  customized  for CDROM in order  to  provide  acceptable 
performance.

     The  development of a standard logical format for  recording 
data  files  on  CDROM disks was taken on by  a  group  of  CDROM 
applications  developers, hardware vendors and computer  vendors. 
The  proposed standard resulting from this effort is  called  the 
High   Sierra   format.  This  format  was   submitted   to   the 
International Standards Organization (ISO) for consideration  and 
approved  on October 5, 1987. The format used for the  PDS  CDROM 
disks is dated May 28, 1986, and differs slightly from the  final 
ISO standard. Microsoft and other CDROM software developers  have 
committed to supporting this preliminary version of the format in 
later  software  releases. However, software developed  by  other 
vendors  to  support the ISO format (DEC for  example)  will  not 
support the format of these disks.


                            Chapter 3

                       IMDISP INSTALLATION


     IMDISP requires an IBM PC, XT, AT or 100 percent  compatible 
with  512K of base memory. It supports several  graphics  display 
devices,  including  the  Enhanced Graphics  Adapter  (EGA),  the
Video Graphics  Array  (VGA), the Professional  Graphics  Adapter  
(PGA),  and  the  Color  Graphics  Adapter  (CGA).  The  hardware 
environment  in which  the program  has been developed and tested 
includes and  AT class computer,  deluxe or  enhanced  EGA  board 
with 256K of memory, and multisync or multiscan monitor.

3.1 PROGRAM SETUP

     The IMDISP program can be run from a floppy or hard disk. To 
use  the program from a floppy disk, insert the program  disk  in 
the  A: or B: drive and type the MSDOS command: "A:" or  "B:"  to 
set the floppy disk as the default drive. To use the program from 
hard disk first create a directory to hold the IMDISP files.  Use 
the  MSDOS command "MKDIR \IMDISP" to create a directory to  hold 
the programs. Use the "CHDIR \IMDISP" command to make IMDISP  the 
default directory. Insert the distribution floppy disk in  floppy 
disk  drive A:. Now type "COPY A:*.*" to copy the files from  the 
distribution  disk to your hard disk. You should now be  able  to 
run  all examples from that directory on your hard disk.  If  you 
wish  to use IMDISP from other directories, you need  to  include 
the  IMDISP directory in your MSDOS "PATH" command. This  command 
provides MSDOS with a list of directories to search when  looking 
for  a  program  file  to run. If you wish  to  run  IMDISP  from 
different  directories, the \IMDISP subdirectory should be  added 
to  the  PATH command in your AUTOEXEC.BAT file.  A  sample  path 
command would look like this:

    PATH=C:\DOS;C:\UTIL;C:\WORDSTAR;C:\IMDISP

     The  sample  batch  files and special  pointer  label  files 
included  on the distribution disk will only run if your  current 
default directory is \IMDISP.

     You  may want to add a line to your AUTOEXEC.BAT file  which 
will  allow you to abort the display program while running  batch 
files or displaying large image files. If the command  "BREAK=ON" 
is  placed  in  CONFIG.SYS,  you  will  (sometimes)  be  able  to 
terminate the IMDISP program by typing the control and break keys 
simultaneously. Different computer systems offer varying response 
to  the  control-break command, and the use of this  command  may 
effect other programs you use.

3.2 CDROM SETUP

     To use the IMDISP program with PDS CDROM disks you will need 
a  CDROM  reader, interface board, and software provided  by  the 
vendor  which will make your CD Reader look like a disk drive  to 
your  PC.  The details of setting up your hardware  and  software 
configuration  are  beyond  the scope  of  this  manual,  however 
several aspects of setup will be reviewed.

     There  are  many  potential  pitfalls  in  setting  up  your 
hardware and interface board. Read the directions carefully,  and 
don't  assume that "default" switch settings are  correct.  Check 
all  switches  to  see that they correspond  to  the  recommended 
settings.

     To  work  properly with the batch command  and  label  files 
provided  with  IMDISP, your CDROM drive should be set up  to  be 
drive letter "L:". Most vendor software allows you to select  the 
drive letter which will be assigned to the CDROM reader.

3.2.1 Microsoft Extensions

     If  you are using the Microsoft Extensions you will  load  a 
CDROM  device  driver  as part of your CONFIG.SYS  file  (or  two 
drivers  if  using the Philips or DEC readers) with a  line  like 
this:

     DEVICE=HITACHI.SYS /D:CDROM1 /N:1 

This command assumes that the driver file "HITACHI.SYS"is located 
in  your ROOT directory. The /D:CDROM1 switch assigns  a  logical 
name CDROM1 to the drive. A name must be supplied, and is used to 
identify this device, in case more than one CDROM drive is  being 
used on your system. The name should not be the same as the  name 
of any file stored on your system. An attempt to open a file with 
the  same  name as the device driver will result  in  the  device 
driver being opened, not the file. The /N:1 switch indicates that 
this  is drive 1. This switch is used since some CDROM  interface 
cards support multiple drives.

     Other commands which should be included in CONFIG.SYS if you 
are using a CDROM drive with the Microsoft Extensions are:

     LASTDRIVE=Z 
     FILES=30
     BUFFERS=50


     The LASTDRIVE command tells MSDOS to allow for enough  drive 
letters to support the CDROM drive, plus any other drives on your 
system. Using LASTDRIVE=L should also work in most circumstances. 
The  files and buffers specifications provide  sufficient  system 
work area to support CDROM operations.

     You  must  also execute a program  called  MSCDEX.EXE  which 
allows  access to the CDROM drive as if it were a disk  drive  on 
your system. This command can be put in your AUTOEXEC.BAT file so 
that it is automatically run whenever you start-up your computer. 
The command format is:

     MSCDEX /D:CDROM1 /L:L /M:20 /V /E

     Several  MSCDEX command switches are illustrated.  The  /L:L 
command  assigns  the drive name L: to the CDROM  drive.  The  /D 
switch  gives the device name of the CDROM drive (which  must  be 
the  same  name  used  in  the  device  name  parameter  of   the 
"DEVICE=CDROM.SYS"  command  in the CONFIG.SYS  file.  The  /M:20 
switch  assigns  twenty 2K blocks of memory as a buffer  for  use 
with CDROM data. The /V switch provides verbose messages when the 
installation  program  is run, and /E tells the  program  to  use 
expanded memory for the cache area.

3.2.2 Other Driver Software

     Some   vendors  (Reference  Technology,  TMS)  offer   CDROM 
software  which  is comparable to the Microsoft  Extensions.  Our 
experience  with these software packages is that they modify  the 
internals of MSDOS and may cause unpredictable results with  your 
other  PC software. They often do not support CDROM  applications 
designed  to work with the MSDOS extensions for CDROM and  cannot 
be used with the IMDISP FILE prompt mode.

3.2.3 Problems with CDROM Software

     The  PDS CDROM disks utilize a feature of the  CDROM  format 
standard which provides extended attribute records to define  the 
physical  characteristics  of data files. These records  will  be 
used  by VAX and other minicomputer systems where  the  operating 
system  allows  a  variety of record  formats  (fixed,  variable, 
stream).  Many  of  the earlier implementations  of  High  Sierra 
software  failed to recognize these records, which are placed  at 
the  beginning of a file's data area. If your CDROM software  was 
developed prior to April 1987, it may interpret these records  as 
part of the data file, causing the first 2K bytes of each file to 
appear as meaningless binary data. Users with this problem should 
contact  their hardware or software vendors for updated  versions 
of  the  CDROM software. The IMDISP program has been  patched  to 
recognize and skip over these records on the PDS CDROM disks, but 
these  patches  may not support other CDROM disks  with  extended 
attribute records.

3.3 DISPLAY DEVICE CHARACTERISTICS

     IMDISP  automatically  finds out which display  devices  are 
available  (PGA,  EGA, or CGA) and uses the  one  available.  The 
Enhanced  Graphics Adapter must have at least 128K of  memory  to 
work  properly. Use of the Color Graphics Adapter is  discouraged 
because the pixels have no gray levels, only black or white.

     The  display  coordinates start at (1,1) in the  upper  left 
corner  of the screen; the line direction is down and the  sample 
direction is to the right.

3.3.1 Enhanced Graphics Adapter (EGA)

     The   EGA  is  a  bit-mapped  display  device  providing   a 
resolution  of  350  lines  by 640 samples  of  4-bits  each.  It 
produces  a  digital video signal for each  primary  color  (red, 
green  and blue), The video signal for each color can be  set  to 
one  of four levels, roughly equivalent to off, low,  medium  and 
high.  Thus the number of possible colors (color palette)  is  64 
(4^3). The following table illustrates the colors created by some 
of the different combinations of red, green and blue.

  Red=   off, Green=   off, Blue=   off   results in Black
  Red=   low, Green=   off, Blue=   off   results in Dark Red
  Red=medium, Green=   off, Blue=   off   results in Light Red
  Red=  high, Green=   off, Blue=   off   results in Bright Red
  Red=   low, Green=   low, Blue=   low   results in Dark Gray
  Red=medium, Green=   low, Blue=   off   results in Brown
  Red=medium, Green=medium, Blue=   off   results in Yellow
  Red=medium, Green=medium, Blue=medium   results in Light Gray
  Red=  high, Green=   low, Blue=   off   results in Orange
  Red=  high, Green=  high, Blue=  high   results in White

         Table 3-1: Sample EGA Color Palette Settings


     The  EGA display is limited to only 16 colors out of the  64 
possible, because only 4-bits are used to store each pixel  value 
in memory. This 4-bit pixel value points to an entry in the color 
table  which  represents one of the 64 possible  combinations  of 
red, green and blue which can be displayed.

     Many  of  the  newer EGA boards are  capable  of  displaying 
additional lines and samples when using a Multisync or  Multiscan 
monitor.  The  standard  EGA uses a  16  Mhz  crystal  oscillator 
(something like a clock which regulates the display speed), which 
limits  the video output rate to the equivalent of 640 pixels  by 
350  lines.  The  EGA  circuitry  allows  for  a  faster  crystal 
oscillator to be added to the board (24 Mhz and beyond)  allowing 
about 25 percent more lines to be displayed (480 lines instead of 
350).  A  method for adding this capability to  an  existing  EGA 
board  (for  about  $10  worth of  parts)  is  described  in  the 
September 16, 1986 issue of PC Magazine.

     This mode requires that a multisync or multiscan monitor  be 
attached to the computer, and there is no way for the program  to 
automatically  detect  the  presence  of  the  special   monitor. 
Therefore  this  display mode is invoked by specifying  an  MSDOS 
"ENVIRONMENT"  variable. This is done by issuing an  MSDOS  "SET" 
command at the MSDOS prompt as follows:

    SET EGA480=TRUE

     This command can also be put in your AUTOEXEC.BAT file using 
a  text editor, so that you need not invoke it each time you  run 
IMDISP.   It  should  have  no  effect  on  other  MSDOS   system 
operations.  There  is a chance that adding  this  variable  will 
exceed  the size reserved by MSDOS for environment variables.  If 
so,  you  should  consult  your  MSDOS  manual  to  increase  the 
environment size on your system. The environment variable can  be 
removed with the MSDOS command:

    SET EGA480=

     Where a carriage return is typed immediately after the equal 
sign. The 480 line mode requires an additional 83K of memory  for 
the refresh buffer. If you try this mode and receive the  message 
"Insufficient memory for line buffer", it is probably because you 
have  a  512K memory machine, or have  memory  resident  programs 
operating (like Sidekick or Superkey) which reduce the  available 
memory to less than about 400K. You will need to use the 350 line 
mode  or remove some memory resident programs to operate  in  480 
line mode.

     Users  of the EGA with Multisync and Multiscan monitors  can 
achieve  a  16 gray level display through the use  of  a  special 
device  called the Grayscaler 1, from Avocado Computer, Box  632, 
Yorba  Linda, Ca, 92686, (714) 528-1025. This cable converts  the 
digital  video  signals  produced  by the  EGA  board  to  analog 
signals.  By selecting appropriate EGA palette entries, a  fairly 
good  representation of 16 gray levels can be achieved  (use  the 
palette selection "PAL LOAD GRAY16.PAL" to select this palette).

3.3.2 Video Graphics Array (VGA)

This version (2.1) of the IMDISP program includes support for the 
IBM Video Graphics Array (VGA) display device.  The VGA  produces 
an  analog display with several new color modes.   Of  particular 
interest  to  IMDISP users are the 640 x 480 line  mode  with  16 
displayable  colors (or gray levels) and the 320 x 240 line  mode 
with 256 displayable colors (or 64 gray levels).  This version of 
IMDISP supports the 640 x 480 mode.  

To  set  the VGA display mode you must set  a  MSDOS  environment 
variable prior to executing IMDISP.

To set the environment variable use the MSDOS command:

SET VGA=TRUE

This will put the display in 640 sample by 480 line mode, with 16 
gray  levels or colors displayable from a palette of  256K.   The 
display  is  initialized  with  a  gray  scale  palette,  but   a 
pseudocolor  palette can be invoked with the IMDISP command  "PAL 
PS 0".  The "PALETTE EDIT" command will allow you to step forward 
or  backward  through the 64 available shades  for  each  primary 
color.   See  the  next  section  of  the  IMDISP manual for more 
information on the palette edit function.  

3.3.3 Professional Graphics Adapter (PGA)

     The PGA is a special graphics board developed by IBM for use 
with CAD/CAM applications on the IBM PC. Because its architecture 
is incompatible with the CGA and EGA boards, it has not been well 
received by software developers. The PGA provides an analog video 
signal  with a display resolution of 480 lines by 640 samples  of 
8-bits  each. It provides 16 intensities for each primary  color, 
resulting  in a palette of 4,096 colors (16^3). The  color  table 
allows 256 colors to be displayed simultaneously, however only 16 
gray levels can be selected. 

3.3.4 Color Graphics Adapter (CGA)

     The  CGA  display  is a bit-mapped graphics  device  with  a 
resolution of 200 lines by 640 samples of 1-bit each. It supports 
only 2 colors in this display mode, black and white. This display 
can  be used to get a general idea of the contents of  a  digital 
image,  or for displaying one bit images (graphics  for  example) 
but is not recommended for use with the PDS CDROM images.



                          Chapter 4

                       IMDISP OPERATION

     IMDISP can be used to display images up to several  thousand 
lines and samples with a variety of pixel formats. These  formats 
include  bit (1 bit), nibble (4 bits), byte (8 bits), or  integer 
(16  bits). Integer pixels are assumed to be byte-swapped,  which 
means  that  the  sign and most significant 7 bits  are  in  the 
rightmost  byte,  and  the least significant 8 bits  are  in  the 
leftmost byte. This is the convention used by both the IBM PC and 
VAX  computer hardware families. IBM mainframes and 68000  series 
computers  (Macintosh and Sun, for example)  use  un-byte-swapped 
integers.

     Program  interaction with the user is via commands typed  in 
response to the "COMMAND:" prompt. Most interaction is  performed 
on  the graphic display screen, and program messages are  printed 
over  any  image  display currently on the  screen.  The  REFRESH 
command can be used to restore an image after other commands have 
written  text over the display. The ERASE command can be used  to 
clear  away  the  clutter left by  program  status  messages  and 
previously  displayed  images. The screen  is  not  automatically 
erased after each operation in order that multiple images can  be 
displayed simultaneously, or so a histogram can be placed on  the 
screen with the image.

     IMDISP  is invoked by typing "IMDISP" or "IMDISP  filename", 
where  filename  is the name of an image file to  be  opened  for 
processing  at program start-up. The filename may include a  disk 
drive and path name specification.

     The  program  will blank the display screen  and  display  a 
welcome logo, then the prompt "COMMAND:" will appear in the lower 
left  portion  of the screen. If a filename is  included  in  the 
command invocation, the welcome message is not displayed and  the 
screen will display the COMMAND: prompt.

     Typing  "HELP" at the command prompt will provide a list  of 
IMDISP commands. The most frequently used commands are "FILE"  to 
open  a  file for processing, and "DISPLAY" to display  an  image 
once the file has been opened.

4.1 COMMAND SYNTAX

     The command line syntax is of the form:

     COMMAND KEYWORD1 = VALUE1 KEYWORD2=VALUE2 KEYWORD3 VALUE3 . . .

     The command line may be typed in either upper or lower case. 
The  command  and  the  keyword names may  be  abbreviated  to  3 
characters  in most cases. Any number of spaces may  be  inserted 
between  words, and the keyword and value may be separated  by  a 
space  or an equals sign. Some keywords do not require  a  value. 
All  keywords are optional and have default values.  

4.2  COMMAND DESCRIPTION

     Table  4-1 presents a summary of IMDISP commands.  They  are 
separated  into  3 groups, file  manipulation  commands;  display 
commands  and  program  control commands.  Only  the  capitalized 
letters are required to specify a command.

4.3 OPERATING MODES

     Several  of  the commands invoke special  program  operating 
modes.  These  include  the FILE command when  issued  without  a 
filename  argument  and  the CURSOR,  PROFILE  and  PALETTE  EDIT 
commands.  The FILE mode displays a list of files in the  current 
directory  on the screen for selection. It also contains  several 
subcommands  for  controlling the display of files  on  the  menu 
screen.  In  the CURSOR, PROFILE and PALETTE  EDIT  commands  the 
cursor  keys  (arrow  keys) on the numeric  keypad  are  used  in 
conjunction  with other keys to control program operation.  These 
modes  are  exited  by typing either a  period  '.'  or  carriage 
return.

File oriented commands:

       CD or CHDIR      . . . . to change the default directory
       DIRECTORY        . . . . to perform the MSDOS directory command
       FILE             . . . . to specify the name of the image
       SAVE             . . . . to save the image display to a file
       TYPE             . . . . to perform the MSDOS type command
       LABEL            . . . . to display the image labels

Display commands:

       DISPLAY          . . . . to display the image
       ERASE            . . . . to erase the display
       REFRESH          . . . . to refresh the image plane
       PALETTE          . . . . to adjust the palette for the display
       HISTOGRAM        . . . . to display the histogram of the image
       SET              . . . . to set DN value range
       STRETCH          . . . . to do a linear gray scale stretch
       CURSOR           . . . . to move the cursor around
       PROFILE          . . . . to plot a profile of the image
       TEXT             . . . . to draw text on the image

Program control commands:

       BATCH            . . . . to execute a batch command file
       MENU             . . . . to select images from a menu file
       EXIT or QUIT     . . . . to exit from the program
       HELP             . . . . Display help information
       SYSTEM           . . . . execute an MSDOS command

                 Table 4-1: IMDISP Command Summary

4.4 ERROR HANDLING

     If  an invalid command is issued at the COMMAND: prompt  the 
program will beep and return to the COMMAND: prompt. In  handling 
command  parameters the program takes action on those  parameters 
that are recognized, but ignores invalid parameters. For example, 
issuing a "SET LO = 25 HI = 100" command will not have any effect 
since  the proper parameter names for the SET command are  "DNLO" 
and "DNHI".

     It  is  also  possible  for  certain  system  errors  to  be 
encountered  which  cause  the  program  to  abort  leaving  your 
computer  in  graphics mode. N you are  using  certain  utilities 
which reset the default text mode screen colors (like the  Norton 
Utilities  screen attributes command) you may not be able to  see 
what is being printed on the screen. The simplest approach is  to 
perform  a  warm  boot,  by  typing  the  Ctrl,  Alt,  Del   keys 
simultaneously. Alternately, you can often type IMDISP then  EXIT 
to  reset the computer to text mode. Errors in  processing  image 
files on CDROM, hard disk or floppy disks can cause these aborts.

4.5 COMMAND REFERENCE

     This  section lists all IMDISP commands  alphabetically  and 
describes  their  function,  parameters  which  control   command 
operation,  and provides examples of command use, In the  command 
and parameter description the following conventions are used:

  filename    represents the name of an MSDOS file, and may include 
              an optional drive identifier and path specification.

  n           represents an integer value.

4.5.1 BATCH

     The  BATCH command reads commands from the  specified  batch 
command file. If no file name is specified the current  directory 
is  searched for a file named BATCH.CMD. The CURSOR, PROFILE  and 
PALETTE  EDIT  commands should not be used within  batch  command 
files since they require interactive inputs from the keyboard.

     The BATCH command may take the following argument:

   filename    filename of batch command file.

     A  batch  file is simply a text file containing  a  list  of 
commands,  with each command terminated by a carriage return.  If 
the  command file is created with a word processor,  the  program 
should be used in the non-document mode, to assure that  carriage 
returns  are  embedded  between  command  lines.  An  example  of 
creating a batch file to display the PDS logo image follows.

     At the MSDOS command level type:

     COPY CON TEST.CMD 
     FILE LOGO.IMG
     DISP ZOOM 4 
     DISP ZOOM 2
     DISP 
     DISP SUB 2
     EXIT

     Now  run IMDISP and type"BATCH TEST.CMD" at  the  "COMMAND:" 
prompt.  Make  sure  the  file  "LOGO.IMG"  is  in  your  current 
directory.  The  PDS logo should be displayed on  the  screen  in 
several different sizes.

4.5.2 CD or CHDIR

     The  CD or CHDIR command is used just as it is at the  MSDOS 
command level to change the current default directory.

     The   argument   of  the  CD  command  is  the   path   name 
specification  of  the new default directory.  For  example,  "CD 
\IMDISP\IMAGES"  would make \IMDISP\IMAGES the current  directory 
if  it  exists.  To  change the current  default  drive  use  the 
"SYSTEM"  command  ("SYSTEM  L:"   for  example)  or  the  "FILE" 
command.  If there is not enough memory available for the  system 
command to be executed an error message is displayed.

4.5.3 CURSOR

     The CURSOR command is used to select a point in a  displayed 
image  for  subsequent display commands. When first  invoked,  it 
places  a  small  cursor  symbol at the  center  of  the  screen. 
Depending  on the current contents of the screen, the cursor  may 
be  hard  to see. Moving it with the arrow keys  on  the  numeric 
keypad will help you locate it.

     Whenever  the cursor is moved, the current line  and  sample 
location  of  the cursor and the DN value of the  pixel  at  that 
point  is printed in the lower right portion of the  screen.  The 
cursor  will move 16 pixels in the selected direction unless  the 
movement value is adjusted using the + or  keys.

                        Numeric Keypad Keys
                   -------------------------------
                  |   7   |   8   |   9   | PrtSc |
                  |  Home |  Up   |  PgUp |       |
                   -------------------------------
                  |   4   |   5   |   6   |   -   |
                  |  Left |       | Right |       |
                   ------------------------------- 
                  |   1   |   2   |   3   |   +   |
                  |  End  | Down  |  PgDn |       |
                   -------------------------------

                      Action of Keypad Keys:

                      7 = Move up and left.
                      8 = Move up.
                      9 = Move up and right.
                      4 = Move left.
                      5 = Not active.
                      6 = Move right.
                      1 = Move down and left.
                      2 = Move down.
                      3 = Move down and right.
                      - = Decrement cursor movement value.
                      + = Increment cursor movement value.


             Table 4-2: IMDISP Cursor Keys

     Cursor  mode is exited by typing a "." (period) or  carriage 
return. The cursor position is retained for future use in DISPLAY 
commands  which  use the CENTER option. It is  very  useful  with 
large  images where the entire image may be displayed  using  the 
subsample option, then a point selected for subsequent display at 
full resolution.

     Example:  Type  "FILE  MONTAGE.IMG" followed  by  "DISP"  to 
display  the  MONTAGE.IMG file.  Type "CUR" to enter  the  cursor 
mode,  then move the cursor to the center of the Uranus image  in 
the  upper left corner of the image using the up and  left  arrow 
keys.  Now type "." to exit cursor mode, then type "DISP  ZOOM  4 
CENTER"  which will display Uranus as a large grainy ball on  the 
screen.

4.5.4 DIR

     The  DIR command is used just as the MSDOS dir command.  Its 
argument  is  passed to MSDOS for execution. At the  end  of  the 
directory  listing the screen will display "Type carriage  return 
to  continue:" which will return to the IMDISP command  mode.  If 
there is not enough memory available for the system command to be 
executed an error message is displayed.

4.5.5 DISPLAY

     The  DISPLAY command reads an image file and displays it  on 
the  the screen. If the image is larger than the display  screen, 
the default mode is to display as much of the upper left  portion 
of the image as will fit on the screen. The SUBSAMPLE keyword  can 
be   used  to  select  every  'n'  lines  and  samples  so   that 
representations  of very large images may be displayed. The  ZOOM 
keyword  can  be  used to enlarge a portion of an  image  on  the 
display screen. Keywords can be specified to begin displaying  at 
any line and sample in the image with the SL (starting line)  and 
SS  (starting  sample).  If only a limited number  of  lines  and 
samples  are  to  be displayed the NL (number of  lines)  and  NS 
(number of samples) keywords can be used. The UP, DOWN, LEFT  and 
RIGHT  keywords can be used to display different portions of  the 
image,  relative to the currently displayed portion. The  display 
can also placed at any point on the screen using the DSL (display 
starting line) and DSS (display starting sample) keywords.

     DISPLAY takes the following keywords :

      SUBsample n  a positive integral subsampling factor for
                   displaying images larger than the size of the 
                   screen.  SUB=2 would display an image at half 
                   the resolution.  
  
      If the image lines and samples look like this:

                                  sample values 

                line 1            1  2  3  4  5 
                line 2            6  7  8  9 10
                line 3           11 12 13 14 15    

      Then the command DISP SUB 2 would produce:

                                  sample values

                line 1            1  3  5 
                line 2           11 13 15    

      ZOOM n        a positive integral zoom factor for looking at
                    part of an image close up.  The zoom command 
                    replicates pixels by the integer value specified.  
                    If the image lines and samples look like this:

                                  sample values

                line 1            1  2  3  
                line 2            4  5  6
                line 3            7  8  9

      Then the command ``zoom 2" would produce the following:

                                  sample values 

                line 1            1  1  2  2  3  3  
                line 2            1  1  2  2  3  3  
                line 3            4  4  5  5  6  6  
                line 4            4  4  5  5  6  6
                line 5            7  7  8  8  9  9
                line 6            7  7  8  8  9  9


      CENTER     center the display around current cursor position. 
                 This command is very useful when displaying large 
                 images or when zooming in on selected areas. 
      NL n
      NS n       number of lines or samples from the image file to display

      SL n
      SS n       starting line or sample within the image file to display

      UP n
      DOWN n     adjusts the starting line up or down from the 
                 previous value, thereby moving the display window 
                 up or down in the image.  The default amount to 
                 move up or down is the size of the display.

      LEFT n
      RIGHT n    adjusts the starting sample left or right from the 
                 previous value, thereby moving the display window 
                 left or right in the image
        
      DSL n
      DSS n      start the image display at the specified line and 
                 sample on the display screen.

     Examples: The user wants to display an entire Voyager  image 
(800  x 800) on the display screen then display a portion of  the 
image  at full resolution. Type "FILE MIRANDA1.LBL",  then  "DISP 
SUB  2" to display the entire image at half resolution,  Use  the 
CURSOR  command  to move the cursor to the center of an  area  of 
interest.  Exit  the cursor mode by typing ".", then  type  "DISP 
CENT"  to  display  the selected portion of  the  image  at  full 
resolution.

     The  user wishes to place 2 images which are each 800  lines 
by  800 samples on the screen next to each other. The first  file 
is opened with "FILE IMAGE1.IMG".  The "DISPLAY SUB 4" command is 
given to display every 4th line and sample of the image to create 
a 200 x 200 display. Next the "FILE IMAGE2.IMG" command is given. 
Now a "DISPLAY SUB 4 DSS 201" is given to place the second  image 
on  the screen starting at display sample position 201,  next  to 
the first image.

4.5.6 ERASE

     The command ERASE causes the screen to be erased by  setting 
all  of  the  pixels to 0, which may  not  necessarily  be  black 
depending on the palette setting. 

4.5.7 EXIT

     The  EXIT command exits IMDISP and returns the user  to  the 
MSDOS  operating  system. The contents of the image  display  and 
refresh buffer are discarded.

4.5.8 FILE

     FILE does not take a keyword, just a value which is the file 
name.  The  specified file will be opened, or  an  error  message 
issued  if the file cannot be opened. The capability to  directly 
address  any sector on the CDROM disk by providing  its  physical 
address  (minute, second and sector number) is also available  to 
users of the Microsoft Extensions software.

     If  the  FILE command is specified without a  filename,  the 
program  will  display  a  list of  file  names  in  the  current 
directory.  Each  file name is preceded by a number.  Typing  the 
number  associated  with a file name will select  that  file  for 
processing.  File  names  that  actually  represent  lower  level 
directories  are  indicated  with a <d> symbol  after  the  name, 
Directories  can  be traversed downward by selecting  the  number 
associated  with  a  directory  name.  Upward  traversal  is   by 
selecting  the  item  identified as PARENT DIR.  This  will  move 
upward in the directory hierarchy.

     The  prompt  mode clears the screen and displays a  menu  of 
files  and commands. These commands allows specification  of  the 
default  drive, a file "mask" to use in selecting file names  for 
display and options for moving through the list of files when the 
current directory contain more than 30 files. The top line of the 
display  also  indicates  how  many  files  are  in  the  current 
directory.  After  exiting  the FILE prompt  mode,  the  previous 
contents  of  the  display  screen can  be  recovered  by  typing 
"REFRESH".

     The FILE prompt mode subcommands:

         D       select default disk drive
         M       specify a file selection mask to use in displaying 
                 files on the screen.
         N       display the next set of file names on the screen 
                 if there are more files in the current directory 
                 than can be displayed on one screen.
         P       display the previous set of file names.
         Q       quit the file selection mode and return to IMDISP 
                 command mode.

     The  N, P and Q commands are executed immediately. If the  D 
or M commands are selected, the user is prompted to enter a drive 
letter or file mask.

     If  the file selected by the "FILE filename" or FILE  prompt 
mode has a valid label, either PDS or VICAR2, then the number  of 
lines  and samples and the pixel size will be displayed.  If  the 
file  is unlabeled then the program will prompt for the values  to 
use  for the number of lines and samples, the number of bits  per 
pixel,  and  the  number of header bytes.  PDS  detached  labeled 
images  can  also be displayed. The specified  file  remains  the 
current file until a new FILE command is given. The FILE  command 
resets  the  SET  DNLO and SET DNHI values  to  the  minimum  and 
maximum  for the pixel size (normally 0 and 255). If a  specified 
filename  is  not found in the current directory  then  an  error 
message is displayed.

     If  the  unlabeled  image has a regular format,  that  is  a 
uniform  structure of repeating lines and samples, the  user  can 
specify  this  information  when prompted  by  the  program.  For 
example,  an  image named ASTERIA.DAT with one 1422  byte  header 
block  followed by an image composed of 370 lines by 450  samples 
of 8 bit pixels would be processed as follows:

At  the COMMAND: prompt type "FILE ASTERIA.DAT" The program  will 
display the message:

    Input file does not have a proper label.
    Input number of lines: 370                enter the value 370
    Input number of samples: 450              enter the value 450
    Input size of each sample: 8              enter the value 8
    Input size of header label: 1422          enter 1422 for the 
                                              size of the foreign 
                                              label block).

     The  COPIM  utility can be used to add a PDS  label  to  the 
beginning  of  such a file, so that it can be  used  subsequently 
without having to specify all the parameters separately.

     The  physical address of a data block on the CDROM can  also 
be  specified using the syntax 'FILE "CD:mm:ss:bb"', where mm  is 
the minute, ss the second, and bb the sector block number of  the 
beginning  of the desired data area. The CD:mm:ss:nn must  be  in 
double quotes and the CD must be capitalized! This mechanism  can 
be  used  to access files on non-High Sierra format  disks.  This 
will  only  work  on  systems  using  the  Microsoft   Extensions 
software.

4.5.9 HELP


     HELP  displays the online help message. If followed  by  the 
name  of  a  valid  command  the  message  for  that  command  is 
displayed.  HELP is not provided for MSDOS commands (DIR,  CHDIR, 
CD and TYPE).

4.5.10 HISTOGRAM


     The HISTOGRAM command produces a plot showing the number  of 
pixel  values  in  the image at each DN level. The  range  of  DN 
values  is displayed on the x-axis and the number of  occurrences 
of a specific DN value on the y-axis (See Figure 4-1).

     The  HISTOGRAM command reads through the  image,  calculates 
the  histogram,  and then displays the plot on  the  screen.  The 
histogram is scaled so that the third highest histogram value  is 
used  as  the maximum. It is recommended that  the  SUBSAMPLE  or 
other   subsetting  keywords  be  used  to  speed  up   histogram 
calculation,  which  can be quite slow for large images  and  for 
images  stored on CDROM. Histogram plots are displayed on top  of 
any image currently displayed on the screen, so the user may wish 
to  use  the  ERASE command to clear the screen  prior  to  using 
HISTO.  After  the  histogram  is displayed,  the  image  can  be 
restored using the REFRESH command.

       27582  |            .
              |           .. 
              |          ....
    COUNT     |         .....
              |        .......
              |       .........
              |     ............
              |   ...............
              --+-+-+-+-+-+-+-+-+-+-+-+-+-+-+-+ 
              0      64      128     192     256                
                          DN value

            Figure 4-1: Sample Image Histogram


     By  evaluating  the histogram, the user  can  determine  the 
optimum settings for the SET (DNLO and DNHI) command to produce a 
useful  display.  In  the  example  above,  the  image  data  are 
clustered  between  DN  values  32 and  144.  Using  the  default 
settings  of  the EGA display mode the colors assigned to  the  2 
lowest  color  values and the 7 highest values  (representing  DN 
values from 0 to 31 and from 144 to 255) would not be used  since 
the image contains no pixels with these values.

     By  using the "SET DNLO 32 DNHI 144" command the 16  display 
levels  available on the EGA display would be assigned to  values 
between 32 and 144 rather than distributed evenly from 0 to  255, 
and all 16 colors would be used in the display.

     HISTOGRAM takes the following keywords and arguments:

        SUBSAMPLE  n   a integral subsample  factor 
                       for speeding up histogram use of
                       "HISTOGRAM SUBSAMPLE 4" is always recommended
        NL n
        NS n           number of lines and samples from image
        SL n
        SS n           starting line and sample in image

     Two  special  keywords can be used with  Voyager  or  Viking 
images  on  the PDS CDROM disks.  These  will  extract  histogram 
values  stored  with the image on the CDROM disk and  reduce  the 
time required for the histogram to be generated from more than  1 
minute to about 3 seconds. Note that these commands will not work 
with Voyager image files in the \PLANET\JUPITER\ATMOS  directory, 
or with versions of system software written before April 1987.  

        VOY     use histogram from Voyager CDROM engineering data
        VIK     use histogram from Viking CDROM engineering data

4.5.11 LABEL

The label command prints the labels for the currently selected
image file on the screen.  

4.5.12 MENU

The menu command reads a file containing a list of file names and 
places the user in the MENU mode, where files from this list can be 
selected for display.  The MENU mode is similar to the FILE mode, 
except that the list of files presented is that provided in the menu 
file, rather than from a selected directory.

The MENU mode can be invoked by typing "MENU filename.MNU" at the 
COMMAND: prompt.  It can also be invoked on program startup by typing 
"IMDISP filename.MNU" to initiate the program.  The menu file must
use the ".MNU" extension to startup IMDISP in MENU mode.

Subcommands of the MENU mode are as follows:

# - Enter the number corresponding to a desired file name to select
the file.

P)revious  - display the previous screen of file names
N)ext      - display the next screen of file names
Q)uit      - quit or exit from MENU mode

After selecting and displaying an image, the user can return to the 
current menu by typing "MENU" at the COMMAND: prompt.

A menu file can take either of two formats.  The preferred format is a 
PDS labelled table file containing file names.  A sample file is shown
below:

NJPL1I00PDS100000000           = SFDU_LABEL
FILE_TYPE                      = TABLE
RECORD_FORMAT                  = STREAM
OBJECT                         = FILE_NAME
  TYPE                         = LITERAL
  LENGTH                       = 80
ENDOBJECT
NOTE                           = "Sample MENU file for IMDISP"
END
L:\OCEAN\SCBMEAN.IMG
L:\OCEAN\WCMEAN.IMG
L:\PLDS\TMCH01.DAT
L:\PLDS\DEM.DAT
L:\PLANET\SATURN\ATMOS\C3497355.IMG
<END OF FILE>

A second abbreviated form may also be used, where only the filenames 
are specified in the ".MNU" file.  In this case the file would only 
contain the filenames shown after the END statement in the example 
above.  

4.5.13 PALETTE

     The PALETTE command is used for changing the colors assigned 
to  displayable  color  values.  This is  done  by  modifying  an 
internal  color  table which assigns intensity  values  for  red, 
green  and  blue to a color value, The EGA provides  4  intensity 
values  for each of 3 colors, so that 64 different colors can  be 
created. However, the EGA pixels are only 4-bits each so only  16 
color values can be used simultaneously.

     The palette can be modified using the EDIT command and saved 
and  loaded from a disk file. The edit mode is invoked by  typing 
PALETTE EDIT. With the EGA display, a bar containing 16 colors or 
shades  will  be displayed on the bottom of the screen.  A  small 
square  will appear in the middle of the center color  box.  This 
indicates  that  this  color  value  is  currently  selected  for 
editing.  To  select another color value for  editing,  move  the 
small square to the appropriate color using the "4" (left  arrow) 
and  "6" (right arrow) keys on the numeric keypad. The  color  of 
the current color box is changed with the "R", "G", and "B"  keys 
(for  red,  green,  and blue). Upper case  letters  increase  the 
amount  of  the primary color, and lower case keys  decrease  the 
amount of the color. The "8" (up arrow) and "2" (down arrow) keys 
increase  and decrease, respectively, the amount of  red,  green, 
and  blue simultaneously. Other commands in the palette edit mode 
are the  "s" command,  which  will  shift all colors one value to 
the right, and the  "x" command, which will exchange color values 
(the color setting for color  0 becomes the setting for color 15, 
while 15  replaces  0, the  color setting for color 1 becomes the 
setting  for 14,  while 14  replaces  1, etc.).  The  up and down 
arrow keys can also be used to cycle through the colors available 
in  a  given  display  mode  one  at a time.  Type the "." key or 
carriage return to exit the edit mode.

     PALETTE takes the following keywords and arguments:

        EDIT n           to interactively adjust an n-color palette. 
                         See edit description (above) for details

        PSEUDOCOLOR n    PS = 0 for default palette, 
                         PS = 1 for gray scale palette, 
                         PS = 2 for pseudo color palette
        SAVE filename    saves the specified palette on disk
        LOAD filename    loads the specified palette from disk

     The  default  palette file for LOAD or  SAVE  operations  is 
IMDISP.PAL.  The format of the default color palette when  stored 
in a palette file is as shown below:

NJPL1I00PDS000000784            = PDS_SFDU_LABEL
FILE_TYPE                       = TABLE
RECORD_TYPE                     = STREAM
FILE_RECORDS                    =  28
TABLE_ROWS                      =  16
ROW_COLUMNS                     =   4
COLUMN_NAME                     = (COLOR_NUMBER,
                                   RED_VALUE,
                                   GREEN_VALUE,
                                   BLUE_VALUE)
COLUMN_TYPE                     = (INTEGER,INTEGER,INTEGER,INTEGER)
END
   0   0   0   0
   1  64   0   0
   2 128   0   0
   3 192   0   0
   4 192  64   0
   5 192 128   0
   6 192 192   0
   7 128 192   0
   8   0 192   0
   9   0 192 128
  10   0 128 128
  11   0 128 192
  12   0   0 192
  13 128   0 192
  14 192   0 192
  15 192 192 192

     The  first  column of the palette table is the  color  value 
number  for  the display, and columns 2, 3 and  4  represent  the 
intensity  of  the  red, green and  blue  (respectively)  primary 
colors on a scale of 0 to 255. With the EGA display these  values 
are: 0 = off; 64 = low; 128 = medium; 192 = high.

4.5.14 PROFILE


     PROFILE  plots the DN values of pixels located along a  line 
between  two points in the image, i.e. it creates a graph  of  DN 
value versus pixel along the line joining the two points,  Cursor 
mode is used to select the two endpoints; typing "." or  carriage 
return selects the current cursor position as the endpoint. After 
the endpoints are selected a line is drawn between the points and 
the graph is plotted at the bottom of the screen, showing the  DN 
values  on the x-axis and the positions along the line on the  y-
axis.

4.5.15 QUIT

     Exits  the  program. The contents of the image  display  and 
refresh buffer are discarded.

4.5.16 REFRESH

     REFRESH redisplays the image plane from the refresh  buffer. 
When  images are written to the screen they are also  written  to 
the  refresh buffer. The REFRESH command writes this buffer  back 
to  the screen, thereby erasing any graphics or  text  overlaying 
the  image  on the screen. The refresh buffer  contains  as  many 
lines  from  the display screen as there is room for  in  memory. 
REFRESH  takes,es  no parameters. It can also be used  after  the 
FILE prompt mode to redisplay the contents of the refresh buffer.

     Refresh is commonly used after the HELP command, or after  a 
HISTOGRAM  or PROFILE command to remove text and plots  from  the 
display screen.

4.5.17 SAVE

     The  save  command  copies  the  REFRESH  buffer  (which  is 
normally an exact duplicate of the display screen) to a file.  On 
EGA systems the refresh buffer contains only 4 bits per pixel, so 
specifying BP = 8 will write the 4-bit pixels in full bytes,  but 
does not save full 8-bit pixels even if the input image is an  8-
bit  image,  Use  the COPIM utility program  to  produce  a  full 
resolution 16-bit subset of an 8-bit image.

     SAVE  takes the following arguments and keywords, where  the 
filename must immediately follow the SAVE command:

        filename                    filename of image to save

        NL n
        NS n                        number of lines and samples to save

        SL n
        SS n                        starting line and sample to save
        BP n                        number of bits per pixel in output image

     Example: Save a 200 line by 200 sample area at the center of 
an  image  in the file SMALL.IMG. First use the FILE  command  to 
select and display an input image. Now type:

     "SAVE SMALL.IMG SL 100 SS 210 NL 200 NS 200" 

to save the portion of the image beginning at line 100 and sample 
210 in the new file SMALL.IMG.

4.5.18 SET

     SET is used to display and change the DN (pixel value) range 
that  is  used  to  compress  the  pixel  values  to  the   range 
appropriate  for the display device. The default, which is  reset 
for  each  new  file,  is the full range of  DN  values  for  the 
particular pixel format (e.g. 0 to 255 for byte).

     The results of a SET command will not take effect until  the 
next DISPLAY command is performed.

     Set takes the following keywords:

        DNLOW n
        DNHIGH n   where values less than DNlow are set to  color 
                   value 0, values greater than DNHIGH are set to 
                   the  maximum  color value available,  and  the 
                   color  values between are assigned equally  to 
                   the DN values between Dnlow and DNhi.

     For  example,  using the default color palette  and  an  EGA 
display with 16 color values available, the command "SET DNLO 100 
DNHI 164" will assign DN values below 100 to black and DN  values 
above 164 to white, and spread the 16 color values between the DN 
limits, thus each color value will represent 4 DNs (value 0 =  DN 
100 to 103; value 1 - DN 104 to 107, etc.).

     If  values other than the default are used then  the  images 
will display more slowly because scaling divisions are  required. 
SET with no parameters will display the current values.

     The  DNLO  and  DNHI values are reset  to  the  minimum  and 
maximum for a given pixel size when a FILE command is issued.

4.5.19 STRETCH


     STRETCH  sets the palette to a gray scale stretched  between 
the two specified pixel values. Stretch is most useful on the PGA 
display  where 16 gray levels are available. On the  EGA  display 
the  stretch  command  activates the  gray  level  palette  which 
provides  only 4 gray levels. Use the PAL PS 0 command to  return 
the display to the default palette after performing a stretch.

     STRETCH takes the following keywords :

        LOW n
        HIGh n     the low and high DN values  of the stretch.   
                   

     These  pixel  values refer to the DN values in  the  current 
image display, not necessarily in the original image (scaling may 
have  been involved).   For example with the EGA display  the  DN 
values in the display range from 0 to 15, even if a byte image is 
being displayed.

     The STRETCH command is not recommended for use on EGA systems.

4.5.20 SYSTEM

     The SYSTEM command is used to send a command to MSDOS.


     For  example "SYS L:" will set the L: drive as  the  current 
default  drive. If there is not enough memory available  for  the 
system command to be executed an error message is displayed.  The 
SYS  command will not work on floppy disk systems unless the  file 
"COMMAND.COM"  is  present  on the floppy disk  with  the  IMDISP 
program.

4.5.21 TEXT

The text command can be used to display a string of text on the 
screen.  The text string can be entered on the command line, enclosed 
in apostraphies or quotes (e. g., TEXT `This is a text string').  
If the text string is not entered on the command line the program will 
prompt for the string to be displayed.  

Once the command is issued and the text string entered the program is 
placed in CURSOR mode so that the display position can be selected.  
This is done by using the arrow keys to move the cursor to the desired 
location.  After the position is selected, the user types a period (.) 
or carriage return and the text will be written on the display screen.

The text command writes over image data in the display and refresh 
buffer, thus the underlying portion of the image is lost.

4.5.22 TYPE


     The TYPE command is used to type the contents of a text file 
on the display screen, using the standard MSDOS type command.

     Its argument is passed to MSDOS for execution. At the end of 
the type operation the screen will display "Type carriage  return 
to  continue:" which will return to the IMDISP command  mode.  If 
there is not enough memory available for the system command to be 
executed an error message is displayed.

4.6 OTHER UTILITY PROGRAMS

     There  are  several utility programs also  provided  on  the 
distribution  disk. These programs can read PDS  labeled,  VICAR2 
labeled,  or  unlabeled  images. The output  images  are  always 
written  with  PDS  ODL  labels.  The  programs  prompt  for  the 
necessary input values.

4.6.1 COPIM

     COPIM  is a simple image copying program. It' can  copy  the 
whole  image, for example to put PDS labels on a foreign  image), 
or  extract a window from the image. It can subsample  the  image 
with an integral subsampling factor. The program prompts for  the 
input  and  output file names, the window to extract  (just  type 
return  for  the whole image), and the  subsampling  factor  (the 
default  is 1). If the input file is not in VICAR2 or  PDS  image 
format  the program will also prompt for the number of lines  and 
samples, pixel size and header size of the image.

     For example, to extract the first 100 lines and samples from 
the file LOGO.IMG the following commands would be used:

     COPIM 
     Input Image: LOGO.IMG
     Lines: 350 Samples: 340 Bits per pixel: 1 
     Output Image: LOGOSUB.IMG
     Starting line and sample, number of lines and samples: 1 1 100 100 
     Line Subsampling factor (1): 1
     Sample Subsampling factor(1): 1


4.6.2 CONVERT

     CONVERT  is  simple  pixel  format  conversion  program.  It 
converts an image to an integer (16 bits), byte (8 bits),  nibble 
(4  bits),  or binary (1 bit) image. It can also perform  a  user 
specified  scaring. The program prompts for the input and  output 
file  names, the output format (must be 1,4,8, or 16  bits),  and 
the  input and output numerical ranges for scaling.  The  default 
scaling values are appropriate for the data types being used.

     For  example, to convert MONTAGE.IMG to an 8-bit  per  pixel 
image and scale the output pixels evenly between the values of  0 
and 127 the following commands would be used:

     CONVERT 
     Input Image: MONTAGE.IMG
     Lines : 350       Samples : 640 Bits per pixel : 4 
     Output Image: MONTBIG.IMG
     Output bits per pixel (1, 4, 8, 16) : 8 
     Input DN range (O 15) :
     Output DN range (O 255) : 0 127

4.6.3 CLEANUP

     The  CLEANUP and CLEANUP2 programs are available  separately 
with  a  user's guide, executables and required data  files.  The 
purpose  of these programs is to clean up "noisy" Voyager  images 
by  removing the dark current. The dark current image  represents 
the ambient noise in the camera system; therefore, removing  this 
noise "cleans up" the original image, making it appear crisper on 
the monitor.



                           Chapter 5


                        COMMAND SUMMARY


     Within this command summary listing, brackets ([])  indicate 
optional  parameters or keywords. Filename is the name of a  file 
in the current directory or a fully qualified filename which  can 
include  drive  letter and pathname. Directory name is  an  MSDOS 
directory   path   specification,  a  valid  directory   mask   a 
specification  containing wild card characters (*, ?)  per  MSDOS 
rules  for wildcard use in the DIRECTORY command. The symbol  "n" 
is used to indicate an integer value.

    BATCH        [filenamel
    CD           [directory name]  [..]
    CHDIR        [directory name]  [..]
    CURSOR
    DIRECTORY    [directory mask]  [/w]
    DISPLAY      [SUB n] [SL n] [SS n]  [NL n] [NS n]  [BP n] 
                 [CENT] [DSL n] [DSS n]
    ERASE
    EXIT
    FILE         [filename] ["CD:mm:ss:bb"I
    HELP         [command name]
    HISTOGRAM    [SUB n] [SL n] [SS n] [NL n] [NS n] [BP n]
    LABEL
    MENU         [filename]
    PALETTE      [EDIT n] [PS n]  [LOAD filename] [SAVE filename]
    PROFILE
    QUIT
    REFRESH
    SAVE         filename [SL n] [SS n] [NL n] [NS n] [BP n]
    SET          [DNLO n] [DNHI n]
    STRETCH      [LO n] [HI n]
    SYSTEM       [MSDOS command]
    TEXT         "text" or 'text'
    TYPE         filename